## Slide 1
DIPARTIMENTO DI INGEGNERIA ELETTRICA E TECNOLOGIE DELL’INFORMAZIONE
SCUOLA POLITECNICA E DELLE SCIENZE DI BASE
TECHNICAL REPORT OF FIELD AND SERVICE ROBOTICS
Motion planning and Control of a quadrotor UAV
Students: Antonio Rescigno Francesco Grasso

## Slide 2
Index
Motion Planning
The Probabilistic Roadmap Method
The A* Algorithm
Path through multiple waypoints
Trajectory Planning
Controllers
The passivity-based controller
Position and Attitude control through PID controllers with a Kalman Filter
2

## Slide 3
A classical problem for robotic navigation is how to efficiently navigate from one point to another and what to do if obstacles are encountered along the way.
Many map based path planning algorithms attempt to solve this problem, all with varying levels of optimality and complexity. The A* algorithm and the Probabilistic Roadmap method (PRM) are used in this report with the aim of finding a path for the UAV in a known environment with the presence of obstacles.
The Probabilistic Roadmap Method gives as result an approximation of the configuration space. The basic idea is to take random samples from the configuration space of the robot, testing them for whether they are in the free space, and use a local planner to attempt to connect these configurations to other nearby configurations. Each rectilinear path between the two points is sampled and each sample is checked for collisions.
The A* algorithm aims to search for the path at the lowest cost from a starting point to an end point through weighted arcs and a heuristic function. During the implementation, the heuristic function was set to 0, with this assumption the A* algorithm is better known as Dijkstra's algorithm.
3
Motion Planning

## Slide 4
The occ_map.m function creates a 3D map of a fixed size and with obstacles inside. It also deals with the plotting of the start and goal positions. The line setOccupancy(omap3D,xyzObstacles,1) allows to define the positions occupied by obstacles by associating the number 1 if the position is occupied, -1 otherwise. The same operation is replicated for the floor, considered as an obstacle.
The function q_rand_gen.m generates a fixed number of random configurations (established by the parameter iter). These points, if they do not collide with any obstacle, are added to the vector representing a subset of Cfree. Precisely for this reason, as mentioned above, the PRM identifies an approximation of Cfree. Also note, how the first and last points of the points_rdmap vector are associated to the start and goal point, respectively.
4
Probabilistic Roadmap Method (PRM)

## Slide 5
In the function seg.gen.m, for each point of the points_rdmap vector and therefore for each configuration of the approximation of Cfree the neighbors (qnear) are calculated through the parameter ds: the distance of each point from all the others is calculated. Therefore, if the distance is smaller of the threshold ds, the neighbors of the i-th point are added in the second column of the vector indx.
The algorithm ensures that the configurations subsequent to the first do not consider as neighbors the points from which they have already been considered as neighbors. In order to avoid useless calculations for the segments and for the plots that make the algorithm less performing: associations such as: 1- 10 and 10-1 are avoided, in fact if the path from the first to the tenth point is already present, the backward path, from the tenth point to the first is not necessary.
The function segm_m, for each pair of neighbors and therefore for each pair of points whose indices are on the lines of the vector indx samples the segment joining the two points. The segments that intersect an obstacle are then discarded while the extremes of the rest are added to the tree vector: the tree vector therefore contains all the points and their neighbors that the robot can reach in a straight line without colliding.
5

## Slide 6
The adjacency matrix was constructed taking into account the connections obtained with the rows of the tree vector and the generic value of an element of the matrix was set equal to the distance between the i-th and j-th points. Of course, if the points are not connected, the value is set equal to 0.
The algorithm then ends with the calculation of the tree_dfs vector, which contains the position of the nodes to reach. Of course, the algorithm does not necessarily end successfully, the path may not be found and in this case, if subsequent iterations do not lead to any improvement, it is necessary to increase the iter or ds parameters. This is equivalent to increasing the number of iterations and therefore the possible configurations but also to increasing the number of neighbors, with the aim of obtaining more paths to reach the goal.
6
The A* Algorithm

## Slide 7
7

## Slide 8
As seen in the initial simulations, the path is much longer than in the last ones, this is due to very low values of iter and of ds ; it should be remembered that the algorithm A* does not necessarily return a result: it often does the opposite when the values of ds or of iter are around 50- 70.
For iter and ds values ,respectively around 200-400 and 100, the path, even with different tests, does not change drastically: this is due to the fact that the algorithm looks for the minimum absolute path, that is the one that joins the starting and ending points with a straight line; with many configurations and neighbors available, the minimum path will tend to approach the straight line joining these two points.
8

## Slide 9
Path through multiple waypoints
In order to test the control algorithms it has been implemented a path with multiple waypoints:
The algorithm uses the same functions presented at the beginning, with one big difference: the A* algorithm this time is not executed only once, but cyclically and the starting and the ending point of the path are updated as waypoints are reached.
9

## Slide 10
Trajectory Planning
The goal of trajectory planning is to generate the reference inputs to the motion control system which ensures that the robot executes the planned trajectories. We have to generate a time sequence of values of the desired trajectory, that is, to specify a timing law in terms of velocities and accelerations at each point. In this case, a trapezoidal velocity profile is assigned, which imposes a constant acceleration in the start phase, a cruise velocity, and a constant deceleration in the arrival phase.
10

## Slide 11
11

## Slide 12
Control
PASSIVITY BASED CONTROL
PID CONTROLLERS WITH KALMAN FILTER AND ADMITTANCE CONTROL
13

## Slide 13
RPY Dynamic Model for the UAV:
The passivity based control allows to avoid the feedback linearization for the angular part, declaring an highest robustness if conpared for istance to the hierarchial or the geometric control.
This assumption is cfonsiderable true since the external disturbances and the unmodelled dynamics effects are not relevant. In this case an observer could be applied to obtain their evaluetion.
Because of the under-actuation of the system, the external motion planner offers 4 outputs.
Therefore, the Passivity Based Control starts by the knowledge of the desired position and the yaw angle and from the angle , the Euler angles are retrieved .
Passivity Based Control
14

## Slide 14
Considering:
and its first and second time derivatives,
and its first and second time derivatives,
retrieved the position, velocity and acceleration errors for the position and the angular part, it is possible to set the control input, thrust and input torques, as follows.
Where:
For =2.8 and =1.6
And =σ
15

## Slide 15
σ represents the coupling paramenter. It is relevant in the trajectory tracking problem.
It must be assumed as positive. High value of coupling parameter allows to avoid the robot vibration. It is chosen equal to 100 in the current project.
The Passivity Based Control allows to obtain good results which satisfy the trajectory tracking task. The absence of an estimator does not prevent successful results , also applying the following external disturbances:
The following graphs show the position error and the attitude one with respect to the time
16

## Slide 16
Increasing the hight of the external disturbances,
and
The passivity-based control obviously decrease in terms of results. The position error increases significantly as shown. Higher values of define the impossibility to follow the desired trajectory.
17

## Slide 17
PID Controllers with Kalman filter and Admittance Control
This control is developed in reference to the linearized system around the equilibrium point, q=0, where :
The dynamic model
Is rewritten in the second order system form
18

## Slide 18
In opposition to the Passivity-Based-Control, the torques vector tau is evaluated as
And it is controlled through the angular velocity because of the following assumption
( , )
The control input for the position and attitude PID controllers
is built by dividing the system in SISO subsystems. This is useful to control both x and , y and , z and .
The PID gains are multiplied by the error generated by the difference between the estimated position and the reference position given by the admittance control.
The Kalman filter is involved into the estimation of the external disturbances which afflict the system.
It also offers an estimation of the state, used by the PID controllers.
The Kalman filter gains are evaluated through the lqr and lqe matlab function.
The covariance matrix of the measurement and process noises are set equal to
W = 100*eye(18); % process noise
V= 10*eye(6); %measurament noise
19

## Slide 19
The Admittance control changes the trajectory tracking goal by considering the external interactions with the robot. It allows to use the estimated forces and to contrast them, allowing the maintenance of the position as desired.
It is modelled as a mass-damping-spring system with
% Apparent Inertia
m_admittance = 1.2;
M = eye(3)*m_admittance;
% Desired Damping
d_admittance =0.9;
Damp = eye(3)*d_admittance;
% Desired Stiffness
stiff = 0.9;
K = stiff*eye(3);
20

## Slide 20
In comparation with the Passivity-Based-Control, the simulations are done considering external
forces equal to:
The position error and the orientation error linked to the first simulation are shown.
21

## Slide 21
The previous graph represents the external forces estimated by the Kalman filter. The comparation between the actual position and the reference position given by the admittance control is reported.
.
22

## Slide 22
The same results are obtained with respect to the increased disturbances in the second simulation
23

## Slide 23
24

## Slide 24
Conclusion
The Passivity Based Control offers better results in terms of position error in condition of small external disturbances, but this error is constant because of the absence of an observer which allows to compensate these effects. The PID controllers, on the other hand, touches higher peak values, but its average is equal to zero.
By increasing the disturbances, these trends are confirmed but for too high values the passivity based control stops to offer satisfying results.
About the orientation, the PID controller shows a lower error than the Passivity Based one. Moreover, the PID control with Kalman filter and admittance control takes in count also the linearization error.